## Slide 1: Adaptive interrupt coalescing patch for NVMe SSD DCAI PRC Xeon SW Customer Engineering, Nov’25 Zeng Jun; Fang Liang

## Slide 2: What is Adaptive Interrupt Coalescing
Heavy small I/O stress on multiple NVMe SSDs can trigger interrupt bursts, possibly up bounding IOPS of those NVMe SSDs with high level of HW spec.
To solve interrupt burst:
  If IOPS continuously larger than threshold (default 500k) and running io queues num equals to or larger than threshold (default 2) in certain period (default 6 cycle with each 1 seconds), automatically enable coalescing interrupt.
  If IOPS continuously less then threshold (default 500k) or running io queues num less than threshold (default 2) in certain period (default 6 cycle with each 1 seconds), automatically disable coalescing interrupt.
  Note: 1. the check threshold 500k is a data get from experiment over multiple NVMe disks (UMIS/Solidigm/Memblaze/SAMSUNG/…). The threshold value talked above can be modified during runtime now.
For use under CNDA024859 : Bytedance

## Slide 3: How the patch works in Heavy WL
System Agent
(Remaps Translates IRQ / Notifies CPU)
CPU Core
Local-APIC
CPU Core
Local-APIC
SSD1
SSD2
SSD3
System Agent
(Remaps Translates IRQ / Notifies CPU)
CPU Core
Local-APIC
CPU Core
Local-APIC
SSD1
SSD2
SSD3
Heavy Workload Problem
(e.g. bs=4k, numjobs=8 iodepth=128)
Coalesce the Interrupts: As shown by the gray dashed line
Interrupt handling details: https://lwn.net/Articles/951186/
Notifies CPU is expensive
Automatically
coalesce interrupt in heavy workload
How the Patch Works – Interrupt Coalescing Enabled
For use under CNDA024859 : Bytedance

## Slide 4: How the patch works in Light WL
System Agent
(Remaps Translates IRQ / Notifies CPU)
CPU Core
Local-APIC
CPU Core
Local-APIC
SSD1
SSD2
SSD3
System Agent
(Remaps Translates IRQ / Notifies CPU)
CPU Core
Local-APIC
CPU Core
Local-APIC
SSD1
SSD2
SSD3
How the Patch Works – Interrupt Coalescing Disabled
Light WL
(bs=4k numjobs=1 iodepth=1 or other qd vaule)
Interrupt handling details: https://lwn.net/Articles/951186/
Automatically
disable coalesce in light Workload
Why low: (1) wait for requests (2) min timeout: 100us
For use under CNDA024859 : Bytedance

## Slide 5: Patches Readiness
5.10.134
6.6
6.12
Kernel
Patch for Green version is ready
Open Euler5.10-60.18
Rocky 5.14.0-162
For use under CNDA024859 : Bytedance

## Slide 6: Patch Major Changes
Description about the changes in new patch
1. use whole device statistics (IOPS & running IO queues number) to do judgement
1) IOPS of the whole nvme device
2) IO queues being used
2. run the checking logic in delayed work
1) the default scheduled cycle is 1000ms and adaptive the threshold IOPS judgement according to the real time of each cycle
2) delayed work scheduled on the last core of the specific numa which the nvme devices belong to
3. check whether the nvme device support interrupt coalescing or not during the initialization, if interrupt coalescing not supported, then not start the delayed work which used to do the check
4. not use the io size as judgement parameter avoid the fluctuations caused by multiple IO size running at the same time
For use under CNDA024859 : Bytedance

## Slide 7: Installation
Steps to install
- git clone related Linux kernel source code
- git apply the patch
- compile Linux kernel
- make install Linux kernel
- reboot OS
How to check if installed successfully
ls –l /sys/kernel/nvme/
If the configurations exists in this folder, it means the patch has been successfully installed.
For use under CNDA024859 : Bytedance

## Slide 8: Configuration
Parameters | Default | Descriptions
coalesce_value | 266 | The coalesce value set to NVME SSD, similar to below command: nvme set-feature /dev/nvme$i -f 0x8 --value=266 -n 0 266 == 0x10a, that means timeout is set to 100us, coalesced request count is set to 0xa. If want to set 0x109, just need to “echo 265 > /sys/kernel/nvme/coalesce_value”
disable | 0 | 0: enable, to enable adaptive interrupt coalescing, “echo 0 > /sys/kernel/nvme/disable” 1: disable, to disable adaptive interrupt coalescing, “echo 1 > /sys/kernel/nvme/disable”
hit_count_before_change | 5 | How many consecutive detection cycles of nvme device busy should be satisfied before changing coalescing status between coalescing and non-coalescing. See more description in high_io_delta and min_running_queues
scan_interval | 1000 | the scheduled period of delayed work which used to do the checking and judgement, with unit in ms. When changing the scan_interval, the high_io_delta will automatically adjust the high_io_delta threshold according to this setting value.
high_io_delta | 500000 | IOPS per nvme device which used to judge whether to set the interrupt coalescing. When IOPS reach or larger than this value and running IO queues larger than the min_running_queues value then mark the nvme device as busy for 1 time else then mark as non-busy for 1 time (will clear the other when 1 is matched). And when the busy time or non-busy time reach the above hit_count_before_change threshold will trigger the operation of setting or clearing the interrupt coalescing feature.
min_running_queues | 2 | The min num of IO queues been used during each check cycle (see scan_interval above). The running IO queues need to equal or larger than this value when want to set the interrupt coalescing.
check_interval | 512 | the IO interval to mark whether a specific IO queue of a specific nvme device is been used or not.
switch_cnt | 0 | Indicate how many time the status has switched between coalescing and non-coalescing. echo 1 > disable will reset this value to 0.
configurations are located in /sys/kernel/nvme/
*Don't change the value before you really know what you are doing.
For use under CNDA024859 : Bytedance

## Slide 9: Patch with 16x UMIS UH812a PCIe Gen5 Reference Performance Data
容量 | 规格/Intel平台16盘实测 | 随机读（4k)(QD=1,job=1) |  | 随机读（4k)(QD=32,job=1) |  | 随机写（4k)(QD=1,job=1) |  | 随机写（4k)(QD=32,job=1) |  | 随机混合读写（4k)(QD=16,job=1) | 
 |  | 99% | 99.99% | 99% | 99.99% | 99% | 99.99% | 99% | 99.99% | r_99.9% | w_99.9%
7680G | 单盘规格 | 85 | 85 | 150 | 210 | 10 | 20 | 160 | 210 | 400 | 400
 | kernel |  |  |  |  |  |  |  |  |  | 
 | Intel平台16盘实测-1 | 61 | 71.5 | 95.56 | 141.75 | 5.31 | 13.9 | 73 | 81.69 | 336.56 | 15.94
 | Intel平台16盘实测-2 | 61 | 71.44 | 95.62 | 141 | 5.29 | 13.88 | 59.95 | 70.51 | 321.75 | 15.95
 | Intel平台16盘实测-3 | 61 | 71.5 | 95.5 | 140.75 | 5.28 | 13.82 | 60.03 | 70.66 | 334.25 | 16.02
 | 3轮平均值 | 61 | 71.48 | 95.56 | 141.1666667 | 5.293333333 | 13.86666667 | 64.32666667 | 74.28666667 | 330.8533333 | 15.97
 | 3轮平均值-规格达成 | 139.34% | 118.91% | 156.97% | 148.76% | 188.92% | 144.23% | 248.73% | 282.69% | 120.90% | 2504.70%
容量 | 规格/Intel平台16盘实测 | IO场景 |  |  |  |  |  |  |  | 
 |  | 顺序读（128k)-MB/s | 顺序写（128k)-MB/s | 随机读IOPS（4k)-k | 随机写IOPS（4k)-k | 随机混合读写IOPS（4k70读30写)-k | 随机读QD1时延（4k)-us | 随机写QD1时延（4k)-us | 顺序读QD1时延（4k)-us | 顺序写QD1时延（4k)-us
7680G | 单盘规格 | 14800 | 10000 | 3100 | 410 | 696 | 55 | 9 | 8 | 9
 | 16盘规格 | 236800 | 160000 | 49600 | 6560 | 11136 | 55 | 9 | 8 | 9
 | Kernel |  |  |  |  |  |  |  |  | 
 | Intel平台16盘实测-1 | 238400 | 169600 | 55,108 | 7,691 | 19027 | 53.12 | 5.64 | 6.83 | 5.63
 | Intel平台16盘实测-2 | 238400 | 169600 | 55,118 | 9,037 | 21435 | 53.11 | 5.64 | 6.83 | 5.63
 | Intel平台16盘实测-3 | 238400 | 169600 | 55,112 | 9, 063 | 22130 | 53.10 | 5.64 | 6.83 | 5.63
 | 3轮平均值 | 238400 | 169600 | 55,116 | 8,597 | 20864 | 53.11 | 5.64 | 6.83 | 5.63
 | 3轮平均值-规格达成 | 100.68% | 106.00% | 111.2% | 131.05% | 187.36% | 103.56% | 159.57% | 117.13% | 159.86%
测试FW版本：1092 (UMIS 最近更新的版本，解决IO运行过程中配置聚合概率不生效问题), FIO: thread=0
2路 GNR-SP 64C, HT on, Kernel: 6.6 + 自适应中断聚合Patch, FIO 配合numactrl --localalloc + 绑核 (FIO cpus_allowed参数）
测试FW版本：1092 （UMIS最近更新的版本） | 每个盘片绑八个核，不跨node绑核 (numactl --localalloc)，thread=1，测试前先跑2遍4K随机写数据预埋
2路 GNR-SP 64C, HT on, Kernel: 6.6 + 自适应中断聚合Patch, FIO 配合numactrl --localalloc + 绑核 (FIO cpus_allowed参数） | 
For use under CNDA024859 : Bytedance

## Slide 10: NextSetp
Do more test and target for upstream
For use under CNDA024859 : Bytedance